## Product Data Sheet

# P/N W244P-1552BLB								Made in the USA

## 4PR 23AWG SOLID UNSHIELDED NON-PLENUM 550 MHz CATEGORY 6E BLUE JACKET

## TYPE CMR

CONSTRUCTION

CONDUCTOR:					#23 AWG SOLID BC

INSULATION:					POLYETHYLENE

PAIRING:					TWISTED WITH LEFT HAND LAYS

4 PAIRS CABLED TOGETHER WITH A RIGHT HAND LAY

COLOR CODE:					PAIR 1: BLUE/WHITE, BLUE

PAIR 2: ORANGE/WHITE, ORANGE

PAIR 3: GREEN/WHITE, GREEN

PAIR 4: BROWN/WHITE, BROWN

RIP CORD:					YES

JACKET:						POLYMER ALLOY

SEQUENTIONAL FOOTAGE MARKERS

BLUE			OVERALL O.D.:  0.215" nom.

WEIGHT:						27 lbs/1000ft

MINIMUM BEND RADIUS:				1.3 IN

MAXIMUM PULLING FORCE:			27 LBS

TEMPERATURE:					Installation 0 to 60°C / Operation: -20°C to 60°C

### INDUSTRY APPROVALS

UL 1581, UL 1666, CM, CMR, IEC 332-1, CSA, ETL

UL & c(UL) TYPE CMR

ANSA/TIA/EIA-568-B.2-1 (Cat 6)

ANSI/TIA/EIA-862 (Building Automation)

#### APPLICATIONS

- ATM 155 Mbps

- ETHERNET 10BASE-T, 100BASE-TX, 100BASE-VG, 100BASE-T4 (IEEE802.3), 1000 MBPS 1000BASE-T GIGABIT ETHERNET™(IEEE 802.3)

- 16 MBPS TOKEN RING™ (IEEE 802.5)

#### ELECTRICAL PROPERTIES

CONDUCTOR D.C. RESISTANCE:			9.38 Ohms / 100m  nom. @ 20°C

VELOCITY OF PROPOGATION:			70%

CHARACTERISTIC IMPEDANCE:			100 Ohms ± 15Ω

MUTUAL CAPACITANCE:				5.6nF/100 meters

THIS DRAWING AND/OR SPECIFICATION IS THE PROPERTY OF CONNECT-AIR INTERNATIONAL.  IT IS ISSUED IN STRICT CONFIDENCE ,  AND SHALL NOT BE REPRODUCED , COPIED , OR DISCLOSED TO OTHERS , OR USED AS THE BASIS FOR THE MANUFACTURE OR SALE OF APPARATUS WITHOUT THE PERMISSION OF THE OWNER.

4240 B STREET NW

AUBURN, WA 98001

(800) 247-1978

www.connect-air.com

Updated3/9/16 kz